## Slide 1: The Quantrax Hosted Dialer vs On-Premise Dialer
Notes: (Preparing for RMEx Conversion)

## Slide 2: On-Premise Dialer Overview
The dialer servers are located in your office and connected to your PBX
All the telephony services are located in your office
A phone is installed on the agent’s desk and connected to your PBX
The agent connects to the dialer using your PBX

## Slide 3: Hosted Dialer Overview
The dialer is located in our Data Center and connected to RMEx
All the telephony services are located in our Data Center(s)
A ‘soft-phone’ is installed on the agent’s PC
The agent uses a head-set
The agent does not use your PBX when on the dialer

## Slide 4: The Dialer Server Configuration
CM server
STG server (all-IP)
Call recording index server
Reporting server
Test server
Redundancy for all the above

## Slide 5: The On-Premise Network
PRIs or SIP connections to the PSTN (public switched telephone network)
Two channels per agent
PRIs or IP connections to the PBX
LAN connections between the dialer servers and RMEx

## Slide 6: The Dialer Hosting Network
No PRIs or SIP telephony connections
Unlimited telephony services available on hosted dialer
VPN or direct connection to RMEx hosting service
VPN between dialer and client site
Maximum number of agents limited only by client bandwidth

## Slide 7: On-Premise – Agent Requirements
Every agent needs a phone
The phone must be connected to your PBX
The PBX needs software licenses
Every phone needs one or more extension numbers

## Slide 8: Hosted – Agent Requirements
Every agent needs a PC with a connection to your LAN
Every PC needs a static IP address
Every PC needs a headset
You need bandwidth of 100k per agent
A ‘soft-phone’ on the agent’s PC

## Slide 9: On-Premise – Services Included
Hardware may be under warranty
Clients need to provide their own support for servers and networks
Clients need to purchase support for their PBX and phones
Clients need to pay for long-distance usage
Clients need to purchase toll-free numbers and services

## Slide 10: Hosted – Services Included
  All servers, software and telco services
  6000 minutes of calling per agent
  Inbound and toll-free services
  Software maintenance and support
  24 monitoring and support for all servers, telephony services and VPNs

## Slide 11: On-Premise Costs – 10 Agents
PRIs (1) $ 300
Long distance telco services $ 850
PBX and phone maintenance $ ?
Dialer Hardware depreciation $ 278
Dialer Software depreciation $ 556
Dialer Software maintenance $ 250
Dialer check-up service $ 200
Cell phone scrub and TZ Data $ 100
Total $2,534

## Slide 12: Hosted Costs – 10 Agents
Monthly fee @ $305 per agent $3,050

## Slide 13: Other Considerations
Hosted set-up fees $1,500
On-Premise set up fees $5,000-$10,000
PBX costs
Staff costs
Flexibility
Telco services wait times

## Slide 14: Flexibility
10 agents this month
12 agents in January
15 agents in February and March
9 agents for rest of year
Inbound agents
Call blasting

## Slide 15: Who Should Use On-Premise?
Clients with fifty agents or more
Clients with in-house telephony and IT expertise
Clients with predictable telephony needs

## Slide 16: Who Should Use Hosted Services?
Clients with outdated infrastructure
Clients with ten agents or less
Clients needing short term extra capacity
Clients needing a backup for an in-house system
Clients with limited in-house technology or telephony expertise

## Slide 17: The Quantrax Hosted Dialer vs On-Premise Dialer
Notes: (Preparing for RMEx Conversion)